## Slide 1
K-Means Image Color Quantization Accelerator
Bao Nguyen | ECE 410/510 | Spring 2026
62×
projected speedup
What am I doing?
• Custom chip: reduces any photo to 16 colors by grouping similar pixels
How is it done today?
• CPU takes ~9 sec/image using <1% of its power
• 46% of runtime spent waiting for data from memory
What am I doing differently?
• Memory & math sit side-by-side — no waiting
• 16 TB/s bandwidth → ~62× speedup
Accomplished so far
• Benchmarked CPU baseline, found bottleneck
• Distance engine, AXI4-Lite & compute core all passing sim
What's next?
• Full system integration + timing verification
• Compare vs 9-sec baseline → declare success
Roofline — CPU vs PIM Accelerator
System Architecture
Bliss.jpg — Original (left) vs K-Means K=16 colors (right)
Notes: WHAT AM I DOING?
"I'm building a custom chip that takes any photo and compresses it down to just 16 colors — by grouping similar pixels together. Think of the Bliss photo on the right — that's the original, and that's what it looks like with only 16 colors."
HOW IS IT DONE TODAY?
"Right now this runs on a regular CPU and takes about 9 seconds per image — but the CPU is barely doing any work. Less than 1% of its computing power is being used. The bottleneck is memory — the CPU spends almost half its time just waiting for data to load."
WHAT AM I DOING DIFFERENTLY?
"Instead of a CPU, I'm designing a chip where the memory and the math units sit right next to each other — so there's no waiting. You can see that in the roofline plot — on the CPU the kernel sits way down in the memory-bound zone, but on my accelerator it flips to compute-bound. That's where the 62x speedup comes from."
WHAT HAVE I DONE SO FAR?
"I've measured the CPU baseline, confirmed where the bottleneck is, and written all the hardware — the distance engine, the memory interface, and the compute core — all passing simulation."
WHAT'S NEXT?
"I need to connect all the pieces into a full system, verify timing, and then measure actual throughput to prove the speedup is real."
---
TIP: Linger on the Bliss before/after when you first show it — it's your best visual hook.
Total target: ~60 seconds.