## Slide 1
CF06 CLLM
4×4 Binary-Weight Crossbar MAC Unit in SystemVerilog
ECE 410/510 Spring 2026 · Bao Nguyen · LLM: Claude Sonnet 4.6
1 / 7
Notes: So for CF06 CLLM I had Claude Sonnet 4.6 generate a 4-by-4 binary-weight crossbar MAC unit in SystemVerilog. And then I wrote the testbench, ran the simulation, and all four outputs came out exactly right. So basically I'll go over the design, about the weight encoding, and then the results.

## Slide 2
2 / 7
What is a Crossbar MAC?
Rows carry inputs, columns carry outputs
Each intersection = a weight (+1 or −1)
Formula:
out[j] = Σᵢ weight[i][j] × in[i]
Inputs: [10, 20, 30, 40]
out0: +10+20−30−40 = −40
out1: −10+20+30−40 = 0
out2: +10−20+30−40 = −20
out3: −10−20−30+40 = −20
Notes: So about the crossbar — the idea is that rows carry your inputs and columns carry your outputs, and then at every intersection you have a weight that's either plus-one or minus-one. And so each column just does a dot product every clock cycle. That's the formula at the top.
So for example, take column zero. You get plus-ten from row 0, plus-twenty from row 1, and then minus-thirty and minus-forty from rows 2 and 3 because those weights are negative. And so that adds up to minus-40. You can trace the other three columns the same way — like, the arithmetic is right there on the slide.
So basically the crossbar does all four dot products at the same time, every single clock cycle. That's the whole point of it.

## Slide 3
3 / 7
Module Architecture — crossbar_mac.sv
Ports
in0–in3 8-bit signed
out0–out3 10-bit signed
weight_in 16-bit flat
weight_load 1-cycle pulse
Pipeline
① Weight register (FF)
② Comb. MAC (wires)
③ Output register (FF)
Bit width: 4 × 127 = 508
→ 10-bit signed is safe
Notes: So about the module — there are three stages. The top one is the weight register, and that's pretty much just a flip-flop that latches the 16-bit weight bus whenever weight_load pulses high. And then below that is the combinational MAC — I mean, that's just wires, it computes all four dot products simultaneously with no clock. And then the output register at the bottom latches the results on the next rising edge.
So about the bit width — for example, the worst case is four inputs at plus or minus 127, so 4 times 127 is roughly 508. And then 10-bit signed goes up to 511, so basically that's just enough.
And one thing about the implementation — I had to avoid unpacked arrays inside always blocks because iverilog doesn't support variable bit-selects on them. And so I switched everything to individual scalar wires and it compiled clean.

## Slide 4
4 / 7
Weight Encoding — 16-bit Flat Register
bit (4×i + j) encodes weight[i][j] 1 → +1 0 → −1
Testbench weight matrix:
row 0 [+1, −1, +1, −1] → weight_in bits [3:0] = 4'b0101
row 1 [+1, +1, −1, −1] → weight_in bits [7:4] = 4'b0011
row 2 [−1, +1, +1, −1] → weight_in bits [11:8] = 4'b0110
row 3 [−1, −1, −1, +1] → weight_in bits [15:12]= 4'b1000
Notes: So about the encoding — the whole 4-by-4 weight matrix fits into one 16-bit value. And the rule is pretty simple: bit 4i plus j holds weight[i][j]. So for example, bit zero is weight[0][0], bit one is weight[0][1], and then bit four is weight[1][0], and so on.
So for the testbench weights — row zero is plus-one, minus-one, plus-one, minus-one. And so that maps to bits zero through three being 1, 0, 1, 0, which is exactly 0101. And then you do the same for each row and concatenate them to get the full 16-bit value — like, it's pretty straightforward once you see the pattern.
And the reason I went with a flat register is you load the entire weight matrix in exactly one clock cycle. For example, loading row by row would've cost four cycles and needed an address counter on top of that.

## Slide 5
5 / 7
Testbench Strategy — 2-Cycle Pipeline
① Assert reset
Clear all registers
② weight_load pulse
16-bit weight_in latched
into wreg on posedge
③ Weight stable
MAC computes sum0–sum3
④ Output registered
out0–out3 valid
2 cycles after load
weight_in = {4'b1000, 4'b0110, 4'b0011, 4'b0101}; weight_load = 1; in0=10; in1=20; in2=30; in3=40; @(posedge clk); #1; weight_load = 0; @(posedge clk); #1; // read out0–out3 here
Notes: So about the timing — the output shows up two cycles after you assert weight_load. And so that's the key thing to get right in the testbench.
So basically here's why: on the first rising edge after weight_load goes high, the weight register latches the new weights. But then the output register also clocks on that same edge — and I mean it's still sampling the MAC output from the old weights. And so that first output is wrong.
And then one cycle later the MAC is now computing with the new weights, and then the output register latches the correct result. So for example, if you read the output too early — like after just one cycle — you'd get the wrong answer because the MAC was still using the old weight register.
The waveform shows it pretty clearly — so the orange pulse is weight_load, there's a one-cycle gap, and then the green output goes valid.

## Slide 6
6 / 7
Simulation Results — iverilog -g2012
out0 = −40
+10+20−30−40
✓ PASS
out1 = 0
−10+20+30−40
✓ PASS
out2 = −20
+10−20+30−40
✓ PASS
out3 = −20
−10−20−30+40
✓ PASS
Notes: So all four outputs match exactly. Out-zero is minus-40, out-one is zero, and then out-two and out-three are both minus-20. And for example, out-zero — like, column zero gets plus-ten, plus-twenty, minus-thirty, minus-forty, and so that adds up to exactly minus-40.
So basically the simulation ran clean, the timing worked, and the RTL is correct. 4 out of 4.

## Slide 7
7 / 7
Summary
✓
LLM-generated crossbar_mac.sv using Claude Sonnet 4.6
✓
16-bit flat weight register — bit (4i+j) encodes weight[i][j]
✓
Fully combinational MAC, registered outputs, 10-bit signed
✓
Testbench loads [[1,−1,1,−1],[1,1,−1,−1],[−1,1,1,−1],[−1,−1,−1,1]]
✓
Inputs [10,20,30,40] → Simulation: 4/4 PASS [−40, 0, −20, −20]
Thank you!
Notes: So to wrap up — Claude Sonnet 4.6 generated the core module, and then I made the design decisions about the flat weight register, the scalar ports, and the 2-cycle timing. And so the testbench confirmed all four outputs match the hand-calculated values exactly.
So basically a 4-by-4 crossbar is pretty small, but the structure is the same as what scales up to in-memory computing. The weights are plus or minus one, the dot products are parallel, and the output is registered — roughly the same idea at any size. Thanks.